## Slide 1
THESIS DEFENSE PRESENTATION
The Development of a Mobile Application for Monitoring Poultry Egg Temperature and Security Updates
A Secure, Asynchronous, and Resilient Agricultural Cyber-Physical System
Presenter: Shamsudeen Anuoluwapo Adebayo Objectives: 4 | Outage Buffering: Enforced | Transit Encryption: TLS 1.3

## Slide 2
01 / BACKGROUND & PROBLEM
The Agricultural & Security Gaps
• Thermal Sensitivity: Embryos require tight boundaries (37.0°C to 39.0°C). Hypo/hyperthermia spikes cause complete embryonic mortality.
• Outage Caching Gaps: Existing apps lack edge buffering. Agricultural Wi-Fi dropouts result in complete data gaps.
• Firmware Vulnerabilities: IoT edge nodes run unauthenticated, outdated firmware without lifecycle warnings.
Risk Profile: A single environmental crash or data spoofing attack on unencrypted channels (Blynk/analog setups) can cause total batch failure.

## Slide 3
02 / STUDY FOCUS
Consolidated Research Objectives
• Objective 1: Hardware Edge Node: Build ESP32-based node with DS18B20 digital probes and local FIFO queue caching.
• Objective 2: Cloud Backend & HMI: Develop high-performance asynchronous FastAPI API and Flutter mobile client dashboard.
• Objective 3: Security Update Subsystem: Implement version checks during handshakes to trigger update warnings in HMI.
• Objective 4: Experimental Validation: Benchmark accuracy (MAE), delivery latency, and database recovery rates.

## Slide 4
03 / ENGINEERING DESIGN
System Architecture & Telemetry Flow
• Edge Tier: DS18B20 digital probe captures thermal readings and transmits via 1-Wire to the ESP32 node.
• Transport Tier: ESP32 publishes telemetry data over encrypted MQTT TLS (port 8883) to the broker.
• Cloud Tier: FastAPI processes payload, checks edge versions, updates PostgreSQL, and broadcasts via WebSockets.
• HMI/Alerting Tier: Flutter mobile app displays live telemetry updates, while FCM pushes tray notifications.

## Slide 5
04 / USER INTERFACES
Operator HMI Platforms
• Authentication Cockpit: Enforces secure access control using signed JWT session authorizations.
• Temperature Gauge details: Visualizes real-time sensor read curves and color-coded status circles (Green: safe, Red: abnormal).
• Admin Control Console: Allows systems admin to edit threshold limits, audit log grids, and track active nodes.
Walkthrough scale: Includes 12 Mobile UI Screens and 6 Desktop Web Console Views.

## Slide 6
05 / EMPIRICAL FINDINGS
System Metrics & Performance
• Sensor Precision: Digital DS18B20 calibration trials achieved a Mean Absolute Error (MAE) of 0.24°C (Safe limit: ± 0.5°C).
• Edge Data Recovery: Edge buffer cache queue achieved a 100% data recovery rate during Wi-Fi drops under 100 seconds.
• Data Processing Speed: WebSocket telemetry updates refreshed the UI in 142ms; notification latency was 1.14s over Wi-Fi.

## Slide 7
06 / SYSTEM VALIDATION
Security & Operator Usability
• Firmware Verification Loops: Mismatch check handshakes verified code versions in 120ms, alerting users to required updates.
• Cryptographic Controls: Passwords encrypted using Bcrypt; REST API endpoints secured with JWT tokens.
• Field Usability: Field evaluations with 10 operators yielded a System Usability Scale (SUS) score of 77.5/100 ('Excellent').

## Slide 8
07 / FUTURE ROADMAP
Contributions & Future Scope
• Research Contributions: Bridges the gap between agricultural automation and firmware security lifecycle tracking.
• Limitations Identified: ESP32 restricted to 2.4GHz Wi-Fi; internal RAM caching limits buffer queue to 20 records.
• Recommendations for Future Work: Integrate LoRaWAN for 15km rural range; implement LSTM models for predictive anomaly forecasts; develop automated self-healing OTA updates.