## Slide 1
THESIS DEFENSE PRESENTATION
The Development of a Mobile Application for Monitoring Poultry Egg Temperature and Security Updates
A Secure, Asynchronous, and Resilient Agricultural Cyber-Physical System
Presenter: Shamsudeen Anuoluwapo Adebayo Department of Computer Science | Hatchery Telemetry & Security Subsystem
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 1 of 12

## Slide 2
01 / CONTEXT & PROBLEM
Embryonic Requirements & Existing Vulnerabilities
Biological Incubation Needs
• Optimal egg storage temperature is strictly defined between 37.0°C and 39.0°C (FAO, 2024).
• Temperatures below 35.0°C halt development, leading to structural abnormalities.
• Hyperthermia above 39.5°C denatures embryo proteins within 20-30 minutes, causing complete loss.
Existing Architectural Flaws
• Unbuffered nodes lose data during Wi-Fi drops, common in concrete and metallic hatchery barns.
• Lack of transit encryption allows attackers to eavesdrop on and spoof sensor readings.
• Deployments ignore microcontroller firmware version changes, leaving systems exposed to security exploits.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 2 of 12

## Slide 3
02 / STUDY GOALS
Research Aim & Specific Objectives
Research Aim & Purpose
• To develop a secure, real-time IoT-based mobile application framework (Egg Guardian) for monitoring poultry egg incubator temperatures.
• To implement a tracking mechanism that pushes automated firmware version warning notifications to operators when a mismatch is detected.
Specific Objectives
• Objective 1: Fabricate an ESP32 hardware edge node with DS18B20 digital probes and offline caching queues.
• Objective 2: Build a FastAPI cloud API backend and cross-platform Flutter operator mobile application.
• Objective 3: Construct a security subsystem utilizing Bcrypt, JWT tokens, MQTTS over TLS 1.3, and version warnings.
• Objective 4: Evaluate system accuracy (MAE), data recovery rates, and end-to-end alert propagation latency.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 3 of 12

## Slide 4
03 / IMPLEMENTATION MODEL
Iterative Software Development Life Cycle (SDLC)
Phases 1 - 3: Analysis to Coding
• Requirement Analysis: Mapping hatchery requirements, biological parameters, and security standards.
• System Design: Drafting entity-relationship schemas, UML data flow sequences, and hardware schematics.
• Development: Programming ESP32 firmware in C++, FastAPI routes in Python, and mobile UI in Dart/Flutter.
Phases 4 - 6: QA to Maintenance
• Testing: Running isolated unit evaluations on ring buffers, broker routes, and FCM alerts.
• Deployment: Hosting backend APIs in the cloud, flashing microcontroller nodes, and emulating mobile app runs.
• Maintenance: Adjusting threshold hysteresis values and publishing firmware version update notifications.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 4 of 12

## Slide 5
04 / SYSTEM DESIGN
Cyber-Physical Topology & Data Flows
Physical, Transport, & Edge Caching
• Physical Layer: DS18B20 digital probes connect to the ESP32 node via a 1-Wire bus with pull-up resistors.
• Transport Layer: Node publishes serialized JSON telemetry over encrypted MQTTS (TLS 1.3 over port 8883) to the broker.
• Edge Queue: Rings buffers store data during connection drops to prevent data loss.
Cloud API, Storage, & Mobile HMI
• Asynchronous Cloud: FastAPI processes telemetry, coordinates database writes, and streams data over WebSockets.
• HMI Layer: Operator mobile app listens to WebSockets for real-time charts and registers FCM tokens for push alerts.
• Relay Control: Local edge node triggers backup cooling/heating actuators if thresholds are crossed.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 5 of 12

## Slide 6
05 / RELATIONAL STORAGE
Database Design & Entity Schemas
Identity & Telemetry Logging
• Users Table: Stores user identifiers, unique emails, Bcrypt-hashed credentials, and user authorization roles.
• Temperature Records Table: Logs hardware sensor addresses (DS18B20 ROM string), decimal readings, and timestamps.
• Ensures data integrity with strict primary and foreign key constraints in PostgreSQL.
Security Warning & Message Logs
• Security Alerts Table: Logs event types (e.g., Firmware Mismatch), notification messages, and timestamps.
• Notifications Table: Manages user mappings, alert titles, body content, and delivery statuses.
• Supports high-frequency telemetry logging and audits.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 6 of 12

## Slide 7
06 / HMI PLATFORMS
Operator Android Client & Web Admin Console
Flutter Mobile Handset HMI
• Authentication: Secure user login screen utilizing signed JWT tokens.
• Visual Dashboard: Real-time radial temperature gauges and 24-hour historical trend charts.
• Alert Logs: Scrollable logs displaying warning notifications and device update statuses.
Web Desktop Administration Console
• Telemetry Grid: Administrator tables showing live connection states and statuses across all nodes.
• Historical Audits: Filterable views for inspecting long-term temperature compliance logs.
• Control Console: Secure settings for adjusting temperature threshold limits.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 7 of 12

## Slide 8
07 / CYBER SECURITY
Security Threat Mitigation Matrix
Transport & Account Security
• Eavesdropping: Plaintext telemetry intercepted over public networks. Mitigated by MQTTS/TLS over port 8883.
• Credentials Theft: Stolen passwords compromising user profiles. Mitigated by Bcrypt hashing.
• Session Hijacking: Unauthorized API actions. Mitigated by signed JWT token headers.
Device Integrity & Data Audits
• Vulnerable Code Execution: Exploits on outdated edge devices. Mitigated by version checks and warning banners.
• Telemetry Spoofing: Fabricated optimal values masking chamber failures. Mitigated by secure TLS handshakes.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 8 of 12

## Slide 9
08 / EMPIRICAL RESULTS (PART A)
Thermal Accuracy & Caching Resilience
DS18B20 Calibration & MAE
• Sensor Precision: Calibrated digital DS18B20 probe against a mercury reference thermometer inside an incubation chamber.
• Mean Absolute Error (MAE): Measured at 0.24°C, well within the biological limit of ± 0.5°C.
• Digital 1-Wire signal remains resilient against long cable attenuation and analog noise.
Outage Buffering & Data Recovery
• Edge Caching: Tested node buffer during simulated Wi-Fi outages.
• Outage Recovery Rate: Achieved 100% data recovery for drops up to 100 seconds.
• Extended Outages: Local queue successfully overwrote oldest records first, preserving the 20 most recent readings.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 9 of 12

## Slide 10
09 / EMPIRICAL RESULTS (PART B)
Communication Latency & Usability Scores
Alert & UI Refresh Latency
• WebSocket Delay: Real-time telemetry refreshes mobile charts in 142ms.
• FCM Notification Latency: Pushed alert payloads arrive on mobile handset in 1.14s over Wi-Fi, and 1.41s over 4G.
• Fast response times allow operators to intervene quickly during heating failures.
System Usability Scale (SUS)
• User Acceptance Testing: Field tested system usability with 10 poultry operators.
• SUS Questionnaire: Evaluated interfaces across 10 statements (likert-scale).
• Average SUS Score: Achieved 77.5/100, indicating 'excellent' usability.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 10 of 12

## Slide 11
10 / SUBSYSTEM VERIFICATION
Edge Node Firmware lifecycle Tracking
Version Mismatch Alerts
• Firmware check logic: Backend compares edge node firmware version strings against database targets.
• Execution speed: Handshake version checks complete in 120ms.
• UI Warning Banner: Mismatches render a warning banner in the mobile app and push an FCM notification.
Device Integrity Benefits
• Helps operators identify and update outdated edge nodes.
• Provides version warning checks without complex gatekeeper frameworks.
• Ensures edge nodes run secure, authorized code.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 11 of 12

## Slide 12
11 / SUMMARY & FUTURE SCOPE
Research Contributions & Future Recommendations
Key Research Contributions
• Edge Resilience: Local ring buffers maintain data completeness during Wi-Fi drops without expensive gateway hardware.
• Lifecycle Integration: Integrates security update alerts directly into smart farming telemetry.
Recommendations for Future Work
• LoRaWAN Integration: Replacing Wi-Fi with LoRaWAN to allow long-distance transmission (up to 15 km).
• Predictive Analytics: Deploying server-side LSTM models to forecast heating/cooling failures.
• Self-Healing OTA: Implementing automated OTA patching pipelines.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 12 of 12