## Slide 1
THESIS DEFENSE PRESENTATION
The Development of a Mobile Application for Monitoring Poultry Egg Temperature and Security Updates
A Secure, Asynchronous, and Resilient Agricultural Cyber-Physical System
Presenter: Shamsudeen Anuoluwapo Adebayo Specifications: 4 Research Objectives | Outage Caching Buffers | TLS 1.3 Encryption

## Slide 2
01 / BACKGROUND & PROBLEM STATEMENT
Understanding the Hatchery Challenges
Biological Constraints
• Avian embryo development is highly temperature sensitive ($37.0^\circ\text{C}$ to $39.0^\circ\text{C}$).
• Even brief exposure to hyperthermia ($>39.5^\circ\text{C}$) leads to complete embryo death in 20-30 minutes.
• Manual checks using analog gauges are slow, prone to error, and disrupt internal incubator climates.
Technological Gaps
• Unbuffered agricultural IoT architectures lose all telemetry logs during rural network dropouts.
• Existing smart farming solutions lack secure authentication and transit layer encryption.
• Deployments operate without version checking, leaving nodes running outdated, insecure firmware.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 2 of 8

## Slide 3
02 / STUDY FOCUS
Consolidated Project Objectives
Edge Node
• ESP32 microcontroller.
• Interfaces with digital DS18B20 1-Wire probe.
• Implements local FIFO queue for caching data.
Cloud & HMI
• FastAPI cloud backend.
• Asynchronous non-blocking streaming.
• Flutter mobile HMI and desktop web console.
Security Subsystem
• JWT-based API token authentication.
• Transit encryption via MQTTS over TLS 1.3.
• Handshake version check update notifications.
Experimental
• DS18B20 calibration MAE.
• Outage queue recovery rates testing.
• WebSocket & FCM alerts latency benchmarking.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 3 of 8

## Slide 4
03 / ARCHITECTURAL BLUEPRINT
Layered System Topologies
Physical & Edge Layer
• DS18B20 probe query → ESP32 1-Wire hardware line.
• Local buffer checks: Caches telemetry index ring during network drops (20 points max).
• Connection resumes → Flushes cached records sequentially to the cloud API.
Cloud, Storage & HMI Layers
• FastAPI Server handles asynchronous streaming via Uvicorn.
• EMQX broker handles MQTTS transit over TLS port 8883.
• Broadcasting: Writes to PostgreSQL database, pushes sockets to HMI client, and triggers FCM alert trays.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 4 of 8

## Slide 5
04 / USER INTERFACES
Cross-Platform Operator HMI Walkthrough
Flutter Mobile Handset HMI
• JWT Authentication: Enforces secure operator login, storing sessions in mobile local storage.
• Dashboard Gauge: Real-time radial color coordinates indicating thermal boundaries (Green: safe, Red: abnormal).
• Alert Center: Logs version update statuses and historical warning details.
Desktop Web Console
• Telemetry logs grid: Live administrator tables showing device connections and statuses.
• Historical database queries: Audits rolling 24h temperature data curves.
• Control panels: Secure configurations for adjusting temperature limits ($T_{\text{min}}, T_{\text{max}}$).
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 5 of 8

## Slide 6
05 / EMPIRICAL FINDINGS
Experimental Performance Benchmarks
0.24°C Mean Absolute Error
• DS18B20 probe calibrated against mercury thermometer.
• Safely within the biological incubation limit of ± 0.5°C.
100% Edge Data Recovery
• Edge queue caches all records during Wi-Fi dropouts under 100s.
• FIFO buffer overwrites oldest readings first during extended drops.
142ms WebSocket UI Refresh
• Delivers low-overhead telemetry charts updates directly to client.
• Reduces mobile network bandwidth consumption by up to 60%.
1.14s Alert Latency (Wi-Fi)
• Push notifications delivered via Firebase Cloud Messaging (FCM).
• 4G link latency averaged 1.41s; both under the 2.0s limit.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 6 of 8

## Slide 7
06 / SYSTEM VALIDATION
Security update & Usability Evaluations
Firmware Update warnings
• Verifies firmware version strings during handshake ($120\text{ms}$ execution speed).
• Triggers warnings immediately in UI and FCM trays on mismatch (e.g. running `v1.0.1` instead of `v1.0.2`).
• Guards the edge network from running obsolete, vulnerable code.
User Usability Scores (SUS)
• UAT evaluation conducted with 10 poultry farm operators.
• System Usability Scale (SUS) questionnaire calculates an average score of 77.5/100.
• Corresponds to 'Excellent' usability, indicating intuitive layouts and ready field operations.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 7 of 8

## Slide 8
07 / SUMMARY & FUTURE SCOPE
Research Contributions & Recommendations
Research Contributions
• Edge Data Buffering: Solves telemetry packet loss during Wi-Fi drops without expensive hardware gateways.
• Firmware Security Lifecycle: Integrates update warnings directly into the agricultural monitoring loop.
Future Directions
• LoRaWAN Integration: Replaces 2.4GHz Wi-Fi to extend coverage up to 15km in rural settings.
• Predictive AI (LSTM): Server-side models to forecast heating/cooling failures.
• Self-Healing OTA: Automates microcontroller patching upon version mismatch detection.
Shamsudeen Anuoluwapo Adebayo | Egg Guardian Project | Slide 8 of 8